Sample for Advanced Editing Service

Miniaturization of microwave filters is an important area of focus in the electronics industry. Ceramic laminated filters have been widely used for mobile telephones. Combline filters, especially, have attracted attention because of their compactness, low cost of production, low insertion loss, and high rejection capability. In this study, a combline filter in which both sides of the dielectric substrate are utilized is designed. The combline filter consists of two quarter-wavelength resonators. The coupling between them can be changed locally to generate attenuation poles in the frequency characteristics of the transmission parameter. Strong coupling is achieved by installing a patch conductor on the dielectric substrate, above the resonators. The patch conductor is referred to as a coupling capacitor. A method for installing the coupling capacitor by inserting slots into the ground plane is discussed. This method allows the coupling capacitor to be installed without creating a multilayered structure. As method of inserting slots into a ground plane, a defected ground structure (DGS) has attracting much attention. Broadly speaking, therefore, the proposed structure is a kind of DGS. The filter characteristics are investigated through numerical simulations and experiments. Filters with stepped impedance resonators (SIRs) are also discussed, and effects of the coupling capacitor for an SIR structure are described.

[The above content has been derived from a research article written by Toshiaki Kitamura.]

# Comments

It seems this phrase is not commonly used in the literature. Would you like to use “ceramic filters” instead?

The meaning of this phrase is slightly unclear in the context of the sentence. We suggest using “in designing circuitry for mobile telephones,” provided it conveys the intended meaning.

This phrase appears slightly unconventional. An alternative we can suggest is “frequency characteristics of the filter.”

This sentence does not blend with the flow of the text. We suggest the following alternative sentence: Furthermore, a defected ground structure (DGS) is employed to insert slots into the ground plane.

For better clarity, would you like to use the phrase “filter structure”?